## Slide 1: IPv6

## Slide 2
IPv6 Overview
IPv6 is the sixth revision to the Internet Protocol and the successor to IPv4. IPv6 builds upon the functionality of IPv4,
providing improvements to addressing, configuration and maintenance, and security.
An ipv6 address is a 128 bit Hexadecimal number. Which is represented as 8 Groups/Blocks/Hextets of 16 bits each.
Each group is separated by ‘:’
For Example:- 2001:0DB8:00A2:0000:0000:1AB5:0000:BA2D
64 Bit Host ID
64 Bit Network ID
16 Bit block

## Slide 3
Motivation for IPv6:
Exhausted IPv4 address space:
As of 2011, V4 address space is virtually exhausted (only 4.3 billion addresses) despite NAPT and CIDR. IPv6 has
340 undecillion unique IP addresses.
IPv4 addresses are non-hierarchical:
V4 addresses are non-hierarchical and assigned irrespective of geographical topology. This leads to fragmentation and thus
big routing tables (as of 2010 over 320k route prefixes to be exchanged between backbone routers).
Disproportionate IPv4 address assignment:
IPv4 addresses are assigned disproportionately (2005: USA 75%, Asia only ~10%, China < 1%).
IPv4 address management is difficult:
IPv4 does not really support automatic address assignment (except APIPA). Usage of DHCP means high administrative effort.

## Slide 4
No more NAT (Network Address Translation)
Auto-configuration
No more private address collisions
Better multicast routing
Simpler header format
Simplified, more efficient routing
True quality of service (QoS), also called "flow labeling"
Built-in authentication and privacy support
Easier administration
Benefits of IPv6:

## Slide 5
Rules to Reduce size of IPv6
Rule 1-
Ignore all the leading Zeroes
2001:0DB8:00A2:0000:0000:1AB5:0000:BA2D
So we will get, 2001:DB8:A2:0000:0000:1AB5:0000:BA2D
Rule 2-
Replace all the zeroes of a block with a single 0
2001:DB8:A2:0000:0000:1AB5:0000:BA2D
2001:DB8:A2:0:0:1AB5:0:BA2D
Rule 3-
Remove atleast two or more consecutives zero blocks.
Note:- Double column ‘::’ can be used only once in an IPv6 Address.
2001:DB8:A2:0:0:1AB5:0:BA2D
2001:DB8:A2::1AB5:0:BA2D This is our final reduced IPv6 address
Basics of IPv6

## Slide 6
Binary to Decimal & Hexadecimal
Below is a 128 bit IPv6 address represented in binary format and divided into eight 16-bits blocks:
0010000000000001 0000000000000000 0011001000111000 1101111111100001 0000000001100011 0000000000000000 0000000000000000 1111111011111011
Each block is then converted into Hexadecimal and separated by ‘:’ symbol:
2001:0000:3238:DFE1:0063:0000:0000:FEFB
After applying rules it can be shorten to
2001:0:3238:DFE1:63::FEFB

## Slide 7
Configuring IPv6 Address on a Host
There are 3 Methods to configure IPv6 on a Host-
  1.Static-
    We can configure IPv6 address on a pc manually
  2.Auto-Config-
    In Auto-config the host sends multicast request, then the router replies with its own IPv6 interface configuration.
    Then the host picks up the Network ID from that reply & adds own Interface ID as Host ID.
    3.DHCP Config-
        In this Host request to DHCP for IP configuration & DHCP assign IPv6 address, Gateway & DNS Server ip to the host.

## Slide 8
Classification: IPv6 Address Types

## Slide 9
Unspecified, Loopback, Embedded IPv4
Unspecified address is an all 0 address and cannot be assigned to an interface. It would be typed as ::.
This is only used as a source address to indicate the absence of an actual address.
Loopback Address is all 0’s except for the last bit, which is 1. It would be typed as ::1. It operates the same as the IPv4
127.0.0.1 loopback address.
IPv4 Embedded addresses are IPv6 addresses with an IPv4 address embedded in the low-order 32 bits. They are used
to transition networks from IPv4 to IPv6.
Address Range:
0000:0000:0000:0000:0000:0000:0000:0000/8 to 00FF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF/8

## Slide 10
  2.Link-Local Address-
  Every PC by default has an IPv6 Link-Local address starting with FE80 . We can see it by typing command
ipconfig /all in cmd.
  Link-Local address is only Locally significant means it can be used to communicate on a single Broadcast segment only.
  FE80:0000:0000:0000:0000:0000:0000:0000/10 to FEBF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF/10

## Slide 11
3. Unique-Local Address-
  This type of IPv6 address is globally unique, but it should be used in local communication. The
  second half of this address contain Interface ID and the first half is divided among Prefix, Local Bit,
  Global ID and Subnet ID.
  Prefix is always set to 1111 110. Therefore a Unique local address will always starts with FD or FC
  FC00:0000:0000:0000:0000:0000:0000:0000/7 to FDFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF/7
1
F D

## Slide 12
4. Global Unicast Address-
  This type of address is Globally routable over the internet just like Public IPv4 Address.
  Global Routing Prefix: The most significant 48-bits are designated as Global Routing Prefix which is
  assigned to specific autonomous system.
  The three most significant bits of Global Routing Prefix is always set to 001 & 4th bit can be 0 or 1.
  There a IPv6 public IP will always starts with 2 or 3.
  2000:0000:0000:0000:0000:0000:0000:0000/3 to 3FFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF:FFFF/3
Binary format 0010 0011
Hex. Format 2 3

## Slide 13
Static Routing in IPv6
  Unchanged from IPv4
  Default route is now ::/0
  Cisco IOS Static Routing Example:
  ipv6 route 2001:db8::/64 2001:db8:0:CC::1 110
  Routes packets for network 2001:db8::/64 to a networking device at 2001:db8:0:CC::1 with an administrative distance of 110.
Routing Protocols

## Slide 14
2. Dynamic Routing Protocols in IPv6
  Dynamic Routing in IPv6 is unchanged from IPv4:
  IPv6 has 2 types of routing protocols: IGP and EGP.
  IPv6 still uses the longest-prefix match routing
  IGP
  RIPng (RFC 2080)
  Cisco EIGRP for IPv6
  OSPFv3 (RFC 5340)
  Integrated IS-ISv6 (RFC 5308)
  EGP
  MP-BGP4 (RFC 4760 and RFC 2545)

## Slide 15
IPv6 POC

## Slide 16
Thank You