## Slide 1: A10 Networks ADC Training

## Slide 2: Secure Application Services
aGalaxy
(TPS Mgmt.)
Harmony Controller
(Multi Cloud, Multi Service Mgmt.)
SECURITY
TPS
SSLi
CFW
ADC
CGN
APPLICATION DELIVERY
Automation
Analytics
Self Service
Automation
Policy
Detection

## Slide 3: Agenda
ADC Platform
ADC Concept
L4-L7 Load-balancing
Application Acceleration
WAF
DDOS
VRRP
Troubleshooting

## Slide 4: ADC Platform

## Slide 5: Thunder ADC Product Overview
All inclusive ADC features license
  Availability, Acceleration and Security
Per-app analytics and visibility
  With Harmony Controller
Ultra high density partitioning
  Up to 1,023
Superior hardware model designs
  Up to 36 CPU cores (Intel Xeon)
  Field upgradable SSL option
  SSD for added reliability
Multiple form factors
  Physical, Bare Metal, Hybrid, Virtual/Cloud
Internet
THUNDER ADC
HARMONY
CONTROLLER
Backup Data Center
Availability:
GSLB
High-availability
Health-checks
Security:
DDoS Mitigation
WAF
DAF
AAM
Acceleration:
SSL Offload
TCP Reuse
RAM Caching
Compression
Central Mgmt.
Analytics
Automation
Web App
DNS
Other App

## Slide 6: ACOS: Best-in-Class Performance Scalability
Shared Memory Architecture
Flexible Traffic Accelerator
Switching and Routing
Efficient &
Accurate Memory Architecture
64-Bit Multi-Core Optimized
Optimized
Flow Distribution
CPU
1
Comprehensive Feature Set
Standardized ADC
Application security features
Integrated DDoS feature
High availability
High performance
256+ million concurrent sessions
220+ Gbps throughput
Cluster to over 1 Tbps
Purpose built appliances
Efficient and Flexible Form Factors
Physical, virtual and hybrid
SDN/NFV ready
Small 1-3 U appliances
All inclusive license
CPU
2
CPU
3
CPU
N
Notes: Scalable Symmetric Multi-Core Processing (SMMP)
  Designed to Optimize Resource Utilization & Efficiency
Shared-Memory Architecture (SMA)
  Architected for 64-bit Multi-Core, Multi-Threaded Operations
  Fundamental Benefits: Memory, Processor & I/O Efficiency
  Linear Performance Scalability with x86 Trajectory
Flexible Traffic Accelerator (FTA)
  Multi-Processor Flow Distribution
  Symmetric Distribution of Load Across Cores

## Slide 7: Thunder ADC Hardware Appliances
THUNDER 840
5 Gbps (L4&L7)
200k L4 CPS
1 M RPS (HTTP)
PERFORMANCE
PRICE
THUNDER 1030S
10 Gbps (L4&L7)
450k L4 CPS
2 M RPS (HTTP)
SSL Processor
THUNDER 3040S
30 Gbps (L4&L7)
750k L4 CPS
3 M RPS (HTTP)
SSL Processor
THUNDER 3230(S)
30 Gbps (L4/L7)
1.5 M L4 CPS
7.5 M RPS (HTTP)
SSL Processor
Hardware FTA
THUNDER 3430(S)
42 Gbps (L4/L7)
2.5 M L4 CPS
12 M RPS (HTTP)
SSL Processor
Hardware FTA
THUNDER 4440(S)
80 Gbps (L4&L7)
2.9 Million L4 CPS
15M RPS (HTTP)
Optional SSL Processor
THUNDER ADC HARDWARE APPLIANCES
Entry to Lower Mid Range
See datasheet for complete range
Notes: Mid-range enterprise

## Slide 8: Thunder ADC Hardware Appliances
THUNDER 5330(S)
78 Gbps (L4&L7)
3.1 Million L4 CPS
15 M RPS (HTTP)
PERFORMANCE
PRICE
THUNDER 5440(S)
100/100 Gbps (L4&L7)
4 Million L4 CPS
22 M RPS (HTTP)
SSL Processor
THUNDER 5840-11(S)
100 GbE Ports
115/113 Gbps (L4/L7)
6.2 M L4 CPS
31 M RPS (HTTP)
SSL Processor
Hardware FTA
THUNDER 6440(S)
160/150 Gbps (L4/L7)
5.5 M L4 CPS
31 M RPS (HTTP)
SSL Processor
Hardware FTA
THUNDER 6630(S)
150/145 Gbps (L4/L7)
7.1 M L4 CPS
38 M RPS (HTTP)
THUNDER 7440-11(S)
100 GbE Ports
220/200 Gbps (L4&L7)
10.5 Million L4 CPS
44 Million (HTTP)
SSL Processor
Upper Mid Range to High End
See datasheet for complete range
Notes: Mid-range enterprise

## Slide 9: Thunder ADC Hardware Appliances
* SPE (Security Policy Engine) acceleration included
PRICE
PERFORMANCE
THUNDER 4435 SPE
38/38 Gbps (L4&L7)
3.1 Million L4 CPS
12 M RPS (HTTP)
Hardware FTA, SPE
THUNDER 5435 SPE
78/77 Gbps (L4&L7)
3.7 Million L4 CPS
20 M RPS (HTTP)
Hardware FTA, SPE
THUNDER 6635 SPE (100GbE)
THUNDER 6435 SPE
150/145 Gbps (L4&L7)
7.1 Million L4 CPS
38 M RPS (HTTP)
Hardware FTA, SPE
SPE* Models

## Slide 10: vThunder Software Appliances
PERFORMANCE
PRICE
vThunder
200 Mbps to 100 Gbps
Hypervisors: ESXi, KVM, Hyper-V
Cloud: AWS and Azure
Dynamic provisioning, faster roll out
Scale up or down on-demand
LAB EDITION
ESXi
KVM
Hyper-V
20 Gbps
ESXi
KVM
10 Gbps
ESXi
KVM
8 Gbps
ESXi
KVM
Hyper-V
4 Gbps
ESXi
KVM
Hyper-V
1 Gbps
ESXi
KVM
Hyper-V
ESXi
KVM
Hyper-V
200 Mbps
40 Gbps
ESXi
KVM
100 Gbps
ESXi
KVM
Notes: Mid-range enterprise

## Slide 11: Thunder ADC for Bare Metal Software Appliances
PERFORMANCE
PRICE
Bare Metal (Perpetual Licensing)
  10 Gbps to 60 Gbps
  Dynamic provisioning, faster roll out
  Scale up or down on-demand
  License upgrade option
HIGH-PERFORMANCE
20 Gbps (8 cores)
HIGH-PERFORMANCE
40 Gbps (14 cores)
HIGH-PERFORMANCE
10 Gbps (4 cores)
HIGH-PERFORMANCE
60 Gbps (24 cores)
Notes: Mid-range enterprise

## Slide 12: ADC Concept

## Slide 13: Interface behavior
10.10.10.1/24
192.168.10.1/24
1.1.1.1/24
2.2.2.1/24
interface ethernet 1
ip address 1.1.1.1/24
enable
interface ethernet 2
ip address 10.10.10.1/24
enable
interface ethernet 3
ip address 2.2.2.1/24
enable
interface ethernet 4
ip address 192.168.10.1/24
enable

## Slide 14: Putting interface in same subnet
1.1.1.1/24
vlan 10
untagged ethernet 1
untagged ethernet 2
router-interface ve 10
interface ve 10
ip address 1.1.1.1/24
enable
1.1.1.2/24
1.1.1.3/24

## Slide 15
1.1.1.1/24
1.1.1.2/24
interface ethernet 1
enable
trunk-group 1 lacp
port-priority 100
timeout short
!
interface ethernet 2
enable
trunk-group 1 lacp
port-priority 100
timeout short
!
interface trunk 1
ip address 1.1.1.1 /24
Configuring Trunk

## Slide 16
Server Load Balancing
Provide high availability of services
Share load among multiple servers (load balancing)

## Slide 17: Normal Traffic flow through SLB
Firewall/Router
ADC
Server 1
Server 2
IP = CIP
IP = VIP
IP = SIP
Src IP = CIP Dst IP = VIP
Src IP = CIP Dst IP = SIP

## Slide 18: Topology: L3 (routed) mode w/o SNAT
Source IP | Dest IP
200.0.0.1 | 100.0.0.10
Source IP | Dest IP
200.0.0.1 | 100.0.1.100
Dest IP | Source IP
200.0.0.1 | 100.0.0.10
Dest IP | Source IP
200.0.0.1 | 100.0.1.100
100.0.0.0/24
200.0.0.1
100.0.1.0/24
100.0.1.[100-200]
VIP = 100.0.0.10
SNAT = 100.0.1.50

## Slide 19: Topology: L2 mode w/o SNAT
Source IP | Dest IP
200.0.0.1 | 100.0.0.10
Source IP | Dest IP
200.0.0.1 | 100.0.1.100
Dest IP | Source IP
200.0.0.1 | 100.0.0.10
Dest IP | Source IP
200.0.0.1 | 100.0.1.100
100.0.0.0/24
200.0.0.1
100.0.1.0/24
100.0.1.[100-200]
VIP = 100.0.0.10

## Slide 20: Asymmetric flow Issue
100.0.0.0/24
CIP:-200.0.0.1
VIP1:-100.0.0.10
VIP2:-100.0.0.20
SIP1:-100.0.0.100
SIP2:- 100.0.0.200
Src IP = CIP Dst IP = VIP1
Src IP = CIP Dst IP = SIP1
Src IP = SIP1 Dst IP = VIP2
Src IP = SIP1 Dst IP = SIP2
Src IP = SIP2 Dst IP = SIP1

## Slide 21: Topology: L2 mode with SNAT
Source IP | Dest IP
200.0.0.1 | 100.0.0.10
Source IP | Dest IP
100.0.0.50 | 100.0.0.100
Dest IP | Source IP
200.0.0.1 | 100.0.0.10
Dest IP | Source IP
100.0.0.50 | 100.0.0.100
100.0.0.0/24
200.0.0.1
100.0.0.[100-200]
VIP = 100.0.0.10
SNAT = 100.0.0.50

## Slide 22: Per session Load-balancing
Firewall
ADC
Server 1
Server 2

## Slide 23: Source IP Persistency
Firewall
ADC
Server 1
Server 2
Creates entry in persistency table
CIP = Server1
Matching persistency table
CIP = Server1
CIP

## Slide 24: Issue with Source IP persistency
Firewall
ADC
Server 1
Server 2

## Slide 25: Cookie Persistency
Firewall
ADC
Server 1
Server 2
Insert cookie header and create persistency entry
Cookie1 = Server1
match persistency entry
Cookie1 = Server1
Load-balancing decision

## Slide 26: Cookie Persistency with Load-balancing
Firewall
ADC
Server 1
Server 2
Load-balancing
Persistency match
Load-balancing
Load-balancing

## Slide 27: L4 Load-balancing
Firewall
ADC
Server 1
Server 2
TCP-SYN
TCP-SYN
Server 3

## Slide 28: L7 Load-balancing
Firewall
ADC
Server 1
Server 2
TCP-SYN
TCP-SYN
SYN-ACK
ACK
HTTP:GET
SYN-ACK
ACK
HTTP:GET
Server 3

## Slide 29: Server Load Balancing (SLB)
Thunder SLB configuration has three core elements
  Servers, Service Groups, Virtual Servers (VIPs)
Web
DNS
SMTP
Server
Web
DNS
SMTP
Server
VIP
Service Group - Web

## Slide 30: Putting the configuration together
Web
Server
VIP
slb server S1 192.168.1.10
port 80 tcp
Web
Server
VIP
slb server S2 192.168.1.20
port 80 tcp
VIP
Service Group - Web
Web
Web
slb service-group SG1 tcp
member S1 80
member S2 80
VIP
Service Group - Web
Web
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1

## Slide 31: Default Behaviour
slb server S1 192.168.1.10
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1
ICMP Health checks
TCP Health checks
Round-robin
No Source NAT

## Slide 32: Port Template
Connection limit
Connection rate limit
Request Rate limit
Destination NAT
No SSL
Source NAT
Slow Start
slb template port port_80
conn-limit 10000
conn-rate-limit 100
request-rate-limit 500
dest-nat
no-ssl
source-nat nat
slow-start
slb server S1 192.168.1.10
port 80 tcp
slb service-group SG1 tcp
member S1 80
slb service-group SG2 tcp
member S1 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1

## Slide 33: Server Template
Connection limit
Connection rate limit
Health Check
Spoofing Cache
Slow Start
slb template server server_temp
conn-limit 10000
conn-rate-limit 100
health-check-disable
spoofing-cache
slow-start
slb server S1 192.168.1.10
port 80 tcp
slb service-group SG1 tcp
member S1 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1

## Slide 34: Http Template
Failover URL
Host Switching/URL Switching
Client IP Header Insert
Strict Transaction Switch
Header Erase
Header Insert
Response Content Replace
Compression
Redirect
Redirect Rewrite
slb template http http_template
compression enable
failover-url http://portal.com
insert-client-ip X-Client-IP
strict-transaction-switch
url-switching contains /finance service-group SG1
url-switching contains /tech service-group 80
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb server S1 192.168.1.30
port 80 tcp
slb server S2 192.168.1.40
port 80 tcp
slb service-group 80 tcp
method least-connection
member S1 80
member S2 80
slb service-group SG1 tcp
member S3 80
member S4 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1
template http http_template

## Slide 35: Failover URL
Firewall
ADC
Server 1
Server 2
HTTP Request abc.com
HTTP Redirect to xyz.com
HTTP Request xyz.com
Server 3

## Slide 36: URL Switching
Firewall
ADC
Server 1/SG1
Server 2/SG2
Server 3
url=/finance
url=/tech

## Slide 37: Client IP Header Insert
Firewall
ADC
Server 1
Server 2
Server 3
HTTP Request
Src IP : CIP,Dst IP : VIP
Src IP : NAT-IP,Dst IP : SIP
VIP
NAT-IP
CIP
X-Client IP :- CIP

## Slide 38: Application Acceleration

## Slide 39: Acceleration
Application acceleration for a faster user experience and optimized utilization
Technology for Application Acceleration
TCP Optimization: Improve application performance
RAM Caching: Faster page loads equal more revenue
SSL Acceleration: Secure applications
Compression: Optimize any bandwidth level

## Slide 40
TCP Connection Reuse
Web servers need to manage
  New clients (open new sessions)
  Clients leaving (close sessions)
  Maintain all connected clients sessions
Note: Web browsers keep their TCP connections open - even when all objects have been loaded

## Slide 41: Connection Reuse :: Configuration
!
slb template connection-reuse CR1
timeout 1800
keep-alive-conn preopen 10
!
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1
template connection-reuse CR1

## Slide 42: SSL Acceleration
SSL Offload relieves the server of SSL tasks
Provides faster server response time and higher server scalability
Thunder receives HTTPS client traffic and sends HTTP traffic to the servers
HTTPS
HTTP

## Slide 43: SSL Offloading :: Configuration
!
slb template client-ssl SSL
cert SSL_cert
key SSL_cert
!
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 443 https
service-group SG1
template client-ssl CR1
Import/Create the certificate and Key to A10 thunder
ADC > SSL Management

## Slide 44: SSL Offloading with backend encryption :: Configuration
!
slb template client-ssl SSL
cert SSL_cert
key SSL_cert
!
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 443 https
service-group SG1
template client-ssl CR1
template server-ssl svssl
Import/Create the certificate and Key to A10 thunder
ADC > SSL Management
slb template server-ssl svssl

## Slide 45: RAM Caching
RAM caching optimizes network transactions for the user, network and Web servers
Caches HTTP/HTTPS static and dynamic content in Thunder RAM
Delivers cached objects to clients directly from the Thunder ADC cache, offloading servers
Provides faster client download time and higher server scalability

## Slide 46: RAM Caching :: Configuration
!
!
slb template cache RAM_CACHE
max-cache-size 5
!
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1
template cache RAM_CACHE

## Slide 47: HTTP Compression
Compresses HTTP/HTTPS objects
Uses less bandwidth and provides faster client download time
Thunder ADC HTTP compression
  Compresses objects sent to the clients Note: By default, "text" (such as html/css/js) and "application" (such as doc/xls/ppt/pdf)
  If HTTP compression is enabled on the servers, Thunder ADC transparently offloads this task from servers

## Slide 48: HTTP Compression :: Configuration
!
slb template http HTTP_Compression
compression level 2
!
slb server S1 192.168.1.10
port 80 tcp
slb server S2 192.168.1.20
port 80 tcp
slb service-group SG1 tcp
member S1 80
member S2 80
slb virtual-server VIP1 192.168.1.100
port 80 http
service-group SG1
template http HTTP_Compression

## Slide 49: Question
What is health check ACOS does when you add server port to a server ?
  ACOS completes TCP handshake with Server
  ACOS send RST instead of sending first ACK
  ACOS sends ICMP packets to Server
  ACOS waits for 500 ms for server’s heartbeat

## Slide 50: Question
Select two methods to prevent ACOS from caching a small ‘contact.html’ file ?
  Use URL Hash
  Increase ‘min content size’ in RAM Caching Template
  Specify ‘policy uri /contact.html nocache’ in RAM Caching Template
  Set a different ‘Replacement Policy’ on RAM Caching Template
  Apply ACL
  Use Strict Transaction Switching

## Slide 51: Question
What Role ACOS plays between Client and ACOS device when you configure SSL Offload ?
  Client
  Server
  Relay
  Bridge

## Slide 52: Question
The Don’t Honor Conn Rule option under source-ip persistence template refres to which of the following ?
  Ignore connection limits defined on Source-nat pool
  Ignore connection limits defined on Virtual-Server
  Ignore connection limits defined on Service-Group
  Ignore connection limits defined on Server

## Slide 53: Question
Select three object types that the HTTP Compression feature compresses by default.(choose three)
  HTML
  XML
  JPEG
  MPEG
  TXT

## Slide 54: Question
Which HTTP response does ACOS cache when the RAM caching template is applied to a vport?
  301 Moved Permanently
  200 OK
  404 Not Found
  403 Forbidden
  206 Partial content
  None of the above is true

## Slide 55: Question
Which condition causes a UDP heath check to fail ?
  Port replies with a packet
  Port does not reply
  Port reply with RST/FIN
  Port replies with ICMP error message

## Slide 56: Global Server Load-balancing

## Slide 57
ISP DNS
Root DNS
Authorative DNS
Server-farm
Server-farm
ADC
ADC
Firewall
Firewall
ISP
Client
VIP-1
VIP-2
DNS Redirect
DNS Redirect
DNS Response
GSLB Flow

## Slide 58
ISP DNS
Root DNS
Authorative DNS
Server-farm
Server-farm
ADC
ADC
Firewall
Firewall
ISP
Client
VIP-1
VIP-2
Inbound LLB

## Slide 59
ISP DNS
Root DNS
Authorative DNS
ISP
Client
Inbound LLB
DNS Redirect
DNS Redirect
DNS Response
ISP-A
ISP-B

## Slide 60: Putting the Configuration Together :-GSLB
slb virtual-server DNS_SrvA 192.168.1.51
port 53 udp
gslb-enable
gslb service-ip servicevipA 192.168.1.46
port 80 tcp
gslb service-ip servicevipB 192.168.2.46
port 80 tcp
!
gslb site SiteA
slb-dev acos-a 192.168.1.1
vip-server servicevipA
gslb policy test
no geographic
metric-order health-check weighted-ip
dns logging none
dns server any authoritative
gslb zone dabur.com
policy test
service 80 pulse
dns-a-record servicevipA ttl 0 static
dns-a-record servicevipB ttl 0 static
!
gslb protocol enable controller
!
gslb protocol enable device
!
Site-A
Site-B
slb virtual-server DNS_SrvA 192.168.2.51
port 53 udp
gslb-enable
gslb service-ip servicevipB 192.168.2.46
port 80 tcp
gslb service-ip servicevipA 192.168.2.46
port 80 tcp
!
gslb site SiteB
slb-dev acos-a 192.168.2.1
vip-server servicevipB
gslb policy test
no geographic
metric-order health-check weighted-ip
dns logging none
dns server any authoritative
gslb zone dabur.com
policy test
service 80 pulse
dns-a-record servicevip1 ttl 0 static
dns-a-record servicevip2 ttl 0 static
!
gslb protocol enable controller
!
gslb protocol enable device
!

## Slide 61: Putting the Configuration Together :- LLB
slb virtual-server DNS_SrvA 192.168.1.51
port 53 udp
gslb-enable
gslb service-ip servicevipA 192.168.1.46
port 80 tcp
gslb service-ip servicevipB 192.168.2.46
port 80 tcp
!
gslb site SiteA
slb-dev acos-a 127.0.0.1
vip-server servicevipA
gslb policy test
no geographic
metric-order health-check weighted-ip
dns logging none
dns server any authoritative
gslb zone dabur.com
policy test
service 80 pulse
dns-a-record servicevipA ttl 0 static
dns-a-record servicevipB ttl 0 static
!
gslb protocol enable controller
!
gslb protocol enable device
!
slb virtual-server DNS_SrvA 192.168.2.51
port 53 udp
gslb-enable
gslb site SiteB
slb-dev acos-a 127.0.0.2
vip-server servicevipB

## Slide 62: Web Application Firewall

## Slide 63: Section objectives
WAF Overview
Common Application Security Threats
WAF Deployment Modes
WAF Configuration and Threat Mitigation
WAF Logging

## Slide 64: Attackers Don’t Care About Your Firewall
75% of Internet Vulnerabilities are at the Application Layer -- Source: owasp.org

## Slide 65: WAF Overview
Filters communications between users and web applications
Adds a security layer for examining
inbound user requests
output from web servers
Client
WAF
Malicious request
Drop
Client
WAF
Sensitive information
Strip-off sensitive information

## Slide 66: WAF Operational Modes
WAF supports three Operational Modes
Learning
Used for setting initial thresholds for WAF checks based on known, valid traffic patterns
Should NEVER be used in production environments
Passive
Passive WAF operation that is suitable for production environments
Applies enabled WAF checks without performing WAF actions filtered traffic
Useful for identifying false positives for filtering.
Active
Standard operational mode.
WAF drops or sanitizes traffic based on configured policies
Switching an Active mode template to Learning mode removes all template settings. Best practice is to configure a new template in Learning mode while establishing a baseline for new applications that require testing.

## Slide 67: WAF Learning Mode
Setting | Value
buf-ovf-max-url-len | 15
buf-ovf-max-cookie-len | 0
buf-ovf-max-hdrs-len | 23
buf-ovf-max-post-size | 0
max-cookies | 0
max-hdrs | 7
Allowed-http-methods | GET
Get /HTML1.1
Host: www.example.com
Connection: close
User-Agent: Mozilla/5.0
Accept-Encoding: gzip
Accept: text/html
Cache-Control: no-cache
Setting | Value
buf-ovf-max-url-len | 0
buf-ovf-max-cookie-len | 0
buf-ovf-max-hdrs-len | 0
buf-ovf-max-post-size | 0
max-cookies | 0
max-hdrs | 0
Allowed-http-methods | Null

## Slide 68: Typical Deployment Scenario
Learning mode
Set the thresh for certain WAF option by sending known valid traffic to thunder using staging environment
Passive mode
Place the Thunder in production environment, WAF logs the traffic but does not block it, this mode helps in identifying false positive
Active mode
WAF is configured to take action on traffic violating WAF policies and thresholds
LOG SERVER
LOG SERVER
LOG SERVER

## Slide 69: Mitigation – Definition Files
Pre-loaded files for SQL injection, XSS, Response Codes, Bots and URI Black/Whitelists allow immediate protection against these common threats when checks are enabled
Notes – Default definition files cannot be deleted, edited or re-named. To create custom definitions, use the clone feature and edit as needed. WAF features which require definition files will use these defaults, unless custom files are specified

## Slide 70: Threat Mitigation Configuration – Templates
To configure WAF, navigate to Config Mode > Security > WAF > Template > WAF
Click Add and Enter a Name
Select Deploy Mode
Choose a Logging Template (optional – but needed for accessing WAF data plane log messages)
Enable desired security checks for client requests
  Bind Template to Virtual Port

## Slide 71: WAF Template CLI Configuration Examples
Creating the template
A1(config)#slb template waf <template name>
Configuring Deployment Mode
A1(config-waf)#deploy-mode ?
active Deploy WAF in active (blocking) mode
learning Deploy WAF in learning mode
passive Deploy WAF in passive (log-only) mode
Applying logging template
A1(config-waf)#template logging <template name>

## Slide 72: WAF Template CLI Configuration Examples
Configuring WAF Settings (SQL Injection example)
A1(config-waf)# sqlia-check reject ?
WORD Name of WAF policy list file
<cr>
Hitting return will apply the default SQL definition file. If a custom file has been created, enter the name
Configuring WAF Settings (Credit Card Masking example)
A1(config-waf)#ccn-mask ?
<cr>
See the WAF configuration guide for the full list of template options and features

## Slide 73: Allowed HTTP
Client
WAF
waf template waf1
allowed-http-methods "GET POST HEAD“
slb virtual-server VIP1 20.20.20.1
port 80 http
template waf waf1
service-group SG1
Method
GET
POST
HEAD
Https:GET
Https:DELETE
DROP
Supported Http methods on A10 WAF
• GET
• POST
• HEAD
• PUT
• OPTIONS
• DELETE
• TRACE
• CONNECT
• PURGE

## Slide 74: SQL Injection
WAF
DROP
rule1,(?:\%27)|(?:\')|(?:\-\-)|(?:\%23)|(?:#)
rule2,(?:(?:\%3D)|(?:=))[^\n]*(?:(?:\%27)|(?:\')|(?:\-\-)|(?:\%3B)|(?:;))
rule3,\*/from/\*|\*/insert/\*|\+into\+|\%20into\%20|\*/into/\*| into |into|\*/limit/\*|not123exists\*|\*/radminsuper/\*|\*/select/\*|\+select\+|\%20select\%20| select | \+union\+|\%20union\%20|\*/union/\*| union |\*/update/\*|\*/where/\*
SQL Query=1001' or 1=1#

## Slide 75: Cross-Site Scripting
WAF
DROP
------------
o77,onstop
o78,onsubmit
o79,onunload
s1,script
s2,styl
-----------------------
  <script> alert (‘Attacked’) </script>

## Slide 76: Bot Check
WAF
DROP
------------
a4,adsarobot
a5,ah-ha
a6,aktuelles
a7,alexibot
a8,almaden ------------
  User_Agent = alexibot

## Slide 77: CSRF :- Example
attacker.com
bank.com
<img src ="http://bank.com/transfer.cgi?amt=9999&to=attacker">
<img src ="http://bank.com/transfer.cgi?amt=9999&to=attacker">

## Slide 78: CSRF Protection :- Referer Check
GET / transfer.cgi?amt=9999&to=attacker HTTP/1.1
Host: bank.com
User-Agent: Mozilla/5.0 (Windows; U; Windows NT 5.1; en-US; rv:1.6) Gecko/20040113
Accept: text/xml,application/xml,application/xhtml+xml,text/html;q=0.9,text/plain;q=0.8,image/png,image/jpeg,image/gif;q=0.2,*/*;q=0.1
Accept-Language: en-us,en;q=0.5
Accept-Encoding: gzip,deflate
Accept-Charset: ISO-8859-1,utf-8;q=0.7,*;q=0.7
Keep-Alive: 300
Connection: keep-alive
Referer: http://attacker.com/image.html
waf template waf1
referer-check enable bank.com,partner.bank.com www.bank.com/homepage
WAF
  Referer = attacker.com
DROP
bank.com

## Slide 79: CSRF Protection :- CSRF Form Tagging
Referer header is optional there could be scenario where there might be no referer header
Tag each form sent in response with a unique and unpredictable ID (nonce), and then examine the forms returned by users to ensure that the supplied ID is correct.
waf template waf1
csrf-check

## Slide 80: Form Consistency Check
  If a field is sent to the user, ensure that it is returned by the user.
  If a field is not sent to the user, do not allow the user to add that field and return data in it.
  If a field is a read-only or hidden field, verify that the data has not changed.
  If a field is a list box or radio button field, verify that the data in the response corresponds to one or more of the values in that field.
  Enforce HTML field types and lengths.
waf template waf1
form-consistency-check

## Slide 81: URL Black/White List
Next WAF Feature Check
“/site_images.jpg”
“/datab.html/passwd.cgi”
“/privatepage”
static,^[^?]+[.](?:
?|shtml|js|gif|
|jpeg|png|swf|pif|pdf|css|csv|ico)$
dynamic,^[^?]+[.](?:
|aspx?|jsp|php|pl)(?:[?].*)?$
html
jpg
cgi
pwd_file,^[^?]*(?:
|passwords?)(?:[.][^/?]*)?(?:[?].*)?$
passwd
The WAF examines incoming user requests against the URI White Lists and Black Lists.
These lists define rules to explicitly allow or deny traffic:

## Slide 82: URL Check
WAF
URL1
URL2
URL3
URL4
URL5
  URL9
  DROP
  URL2

## Slide 83: HTTP Check
Regardless of deployment mode, the WAF template automatically enforces a basic, default set of HTTP protocol checks. Following suite of additional checks are available in HTTP compliance check
POST request with Content-Length: 0
Header name with no header value
Several Content-Length headers
Chunked request with Content-Length header
Body in GET or HEAD requests
No Host header in HTTP/1.1 request
Host header contains IP address
Content length should be a positive number
Bad HTTP version
Maximum number of headers
Bad host header value
Maximum number of cookies
Invalid character in Host header
Header contains NULL character
Header contains high-ASCII character
POST with invalid Content-Length header
waf template waf1
http-check

## Slide 84: Buffer Overflow
WAF
Setting | Value
buf-ovf-max-url-len | 30
buf-ovf-max-cookie-len | 15
buf-ovf-max-hdrs-len | 20
buf-ovf-max-post-size | 30
max-cookies | 4
max-hdrs | 10
Allowed-http-methods | GET,POST
Setting | Value
buf-ovf-max-url-len | 25
buf-ovf-max-cookie-len | 15
buf-ovf-max-hdrs-len | 18
buf-ovf-max-post-size | 20
max-cookies | 4
max-hdrs | 10
Allowed-http-methods | GET,POST
Setting | Value
buf-ovf-max-url-len | 20
buf-ovf-max-cookie-len | 12
buf-ovf-max-hdrs-len | 15
buf-ovf-max-post-size | 0
max-cookies | 2
max-hdrs | 9
Allowed-http-methods | GET
Setting | Value
buf-ovf-max-url-len | 10
buf-ovf-max-cookie-len | 12
buf-ovf-max-hdrs-len | 15
buf-ovf-max-post-size | 0
max-cookies | 0
max-hdrs | 8
Allowed-http-methods | GET
Setting | Value
buf-ovf-max-url-len | 0
buf-ovf-max-cookie-len | 0
buf-ovf-max-hdrs-len | 0
buf-ovf-max-post-size | 0
max-cookies | 0
max-hdrs | 0
Allowed-http-methods | NULL
  Cookie count = 2
  Cookie count = 5
  DROP

## Slide 85: URL Options
WAF
  URL = %2Fpasswd%2Ftest
URL=/passwd/test
WAF Policy check
decode-entities Decode entities in internal url
decode-escaped-chars Decode escaped characters such as \r \n \" \xXX \u00YY in internal url
decode-hex-chars Decode hex chars such as \%xx and \%u00yy in internal url
remove-comments Remove comments from internal url
remove-selfref Remove self-references such as /./ and /path/../ from internal url
remove-spaces Remove spaces from internal url

## Slide 86: Hide-Response Headers
WAF
HTTP/1.1 200 OK
Content-Type: text/html; charset=ISO-8859-1
Content-Encoding: gzip
Server:
Cache-control: private, x-gzip-ok=""
Content-length: 1272
Date: Thu, 13 May 2004 10:17:14 GMT
APACHE/2.2

## Slide 87: Hide-Response Headers
WAF
HTTP/1.1 200 OK
Content-Type: text/html; charset=ISO-8859-1
Content-Encoding: gzip
Server: APACHE/2.2
Cache-control: private, x-gzip-ok=""
Content-length: 1272
Date: Thu, 13 May 2004 10:17:14 GMT
HTTP/1.1 200 OK
Content-Type: text/html; charset=ISO-8859-1
Content-Encoding: gzip
Cache-control: private, x-gzip-ok=""
Content-length: 1272
Date: Thu, 13 May 2004 10:17:14 GMT
waf template waf1
filter-resp-hdrs

## Slide 88: Hide-Response Code
WAF
505 error code
waf template waf1
hide-resp-codes allowed_resp_codes
Default allow_resp_codes
(?:1|2|3)\d{2}|40(?:0|1|4|7)|417|503

## Slide 89: CCN/SSN Masking
WAF
-----------------------------------------------------------------------------------------------------------------------------------------------------------5555-4444-3333-2222---------------------------------------------------------------------------------------------
waf template waf1
ccn-mask
ssn-mask
-----------------------------------------------------------------------------------------------------------------------------------------------------------XXXX-XXXX-XXXX-2222-------------------------------------------------------------------------------------------

## Slide 90: WAF Event Logging
WAFs logs two forms of messages:
Configuration events
Indicate that a configuration change has occurred
Data events
Indicate that traffic has matched a WAF template check
By default, only configuration events are logged to the local logging buffer.
Due to a potential high volume of data event messages, external logging must be configured to view events
WAF logging uses standard ACOS external Syslog template configuration
Logging is activated by binding a logging template to the WAF template on a virtual port

## Slide 91: Understanding WAF Messages
WAF log messages can contain the following fields
Timestamp CEF:version|device-vendor|device-product|
device-version|module|event-type|severity|CEF-extension
Sample WAF log message
2013-11-01 18:01:46 local0.info A1 a10logd: [WAF]<6> CEF:0|A10|SoftAX|2.7.1 P2 |WAF|config|2|msg="Template badstoretest: cookie-encrypt ON, cookie-name=CartID, secret=<encrypted>"

## Slide 92: Best Practices
Use Learning Mode in a lab/non-production environment with simulated traffic
Use Passive Mode in production to validate learned traffic profiles or make adjustments
Use Active Mode when satisfied with Passive adjustment result
SQLIA and XSS checks have a “sanitize” option
Scrubs potentially malicious code and forwards request to web server.
Uses more processor cycles than the preferred option of “drop”

## Slide 93: SSLi

## Slide 94: What is the Problem ?
Security Devices can inspect HTTP Traffic
But blind to SSL traffic
Client
Firewall/IPS
Infected Server
Encrypted Traffic
Infected Encrypted Traffic
Client
Firewall/IPS
Infected Server
Clear-text Traffic
Infected Clear-text Traffic

## Slide 95: SSL Performance Impact on Next Gen Firewalls
Chart: 
| Juniper SRX3600 | Stonesoft 3202 | Palo Alto Networks PA-5020 | SourceFire 8250 | Check Point 12600 | Dell SonicWALL E10800 | Fortinet 3600C | SourceFire 8290
2048-bit | 0.36 | 0.76 | 0.79 | 0.83 | 0.87 | 0.94 | 0.94 | 0.96
Column1
Column2
Performance Impact with 2048-bit SSL Ciphers
81%: The average of performance loss across 7 NG Firewalls
Source: “SSL Performance Problems,” NSS Labs

## Slide 96: Solution: SSL Insight (SSLi)
Encrypted Traffic
Clear-text Traffic
Infected, Encrypted Traffic
Infected, Clear-text Traffic
Client
Firewall/IPS
Infected Server

## Slide 97: SSL Insight Overview
Mitigation against intrusion attacks using SSL
SSli solution built on ACOS
Decrypts outbound SSL traffic for inspection
Re-encrypts and forwards traffic to destination
Mechanisms to bypass personal, private connections (banks, health care)
IPv4 and IPv6 supported
SSL Encrypted connection
SSL Encrypted connection
Unencrypted traffic flow
Secure Server
A10 Outside Device/partition
A10 Inside Device/partition
Client

## Slide 98: SSL Insight Certificates
Secure Server
A10 Outside Device/partition
A10 Inside Device/partition
Client
Internal CA
Root/Sub-CA Certificate with Key
Root/Sub-CA Certificate

## Slide 99
Client |  | SSLi_in |  | Clear-text Zone |  | SSLi_out |  | Server | 
SSLi Ladder Diagram: wo/ Cached Certificate
443
8080
8080
443
https://example.com
Client Hello
Client Hello
Server Hello[Server Cert + Public Key, Signed by well-known CA]
SSL Handshake completed
Proxied Server Hello
SSL Handshake completed
Encrypted Request
RST
Client Hello
SSL Handshake completed
Encrypted Request
Encrypted Response
Clear-text Response
Encrypted Response
[Proxied Server Cert + Local Public Key, Signed by local CA]
Cache
Server Hello
Clear-text Request
Notes: Establish SSL connection with the remote server and get the certificate from the remote server
Extract header information from server certificate.
Change the Issuer and the Public Key as defined in Client-SSL-Template.
Re-sign the new certificate using the CA-Certificate as specified in Client-SSL-Template.
Send the reconstructed Server-Hello to client.
Data decrypted and sent in clear-text through the security device.
New SSL session initiated with remote server.
Data encrypted and sent to remote server.
Response is decrypted and sent through the security device.
Response is encrypted again and sent to the client.

## Slide 100
Client |  | SSLi_in |  | Clear-text Zone |  | SSLi_out |  | Server | 
SSLi Ladder Diagram: w/ Cached Certificate
443
8080
8080
443
https://example.com
Client Hello
Proxied Server Hello
SSL Handshake completed
Encrypted Request
Client Hello
SSL Handshake completed
Encrypted Request
Encrypted Response
Clear-text Response
Encrypted Response
[Proxied Server Cert + Local Public Key, Signed by local CA]
Server Hello
Clear-text Request
Cache
Notes: Establish SSL connection with the remote server and get the certificate from the remote server
Extract header information from server certificate.
Change the Issuer and the Public Key as defined in Client-SSL-Template.
Re-sign the new certificate using the CA-Certificate as specified in Client-SSL-Template.
Send the reconstructed Server-Hello to client.
Data decrypted and sent in clear-text through the security device.
New SSL session initiated with remote server.
Data encrypted and sent to remote server.
Response is decrypted and sent through the security device.
Response is encrypted again and sent to the client.

## Slide 101: Layer-2 Topology with 2 Partition
IP:- 10.10.10.50
Subnet :- 255.255.255.0
Gateway :-10.10.10.1
10.10.10.20
10.10.10.1
10.10.10.10
Decrypted traffic
https traffic

## Slide 102: Layer-3 Topology with 2 Partition
IP:- 10.10.10.50
Subnet :- 255.255.255.0
Gateway :-10.10.10.1
10.10.20.1
10.10.20.10
10.10.10.1
Decrypted traffic
https traffic

## Slide 103: Layer-3 Topology with 2 Devices
IP:- 10.10.10.50
Subnet :- 255.255.255.0
Gateway :-10.10.10.1
10.10.20.1
10.10.20.10
10.10.10.1
Decrypted traffic
https traffic

## Slide 104: Layer-3 Topology with Multiple Security devices
IP:- 10.10.10.50
Subnet :- 255.255.255.0
Gateway :-10.10.10.1
10.10.20.1
10.10.20.10
10.10.10.1
Decrypted traffic
https traffic

## Slide 105: SSL Certificate
Go to File and create new Database

## Slide 106: SSL Certificate
Go to Certificate and click on new Certificate
Go to Subject and Fill the details
Click on Generate new Key

## Slide 107: SSL Certificate
Go to Certificate export the certificate in PKCS#12 format
Fill the export format
Export certificate in PEM format

## Slide 108: SSLi Wizard

## Slide 109: SSLi Wizard

## Slide 110: SSLi Wizard

## Slide 111: Aflex

## Slide 112: Overview:
What is an aFlex?
  TCL based script which is applied under a vPort associated with a Virtual-IP
  gives you flexibility in doing things that you may not be able to achieve using CLI.
What are some scenarios where we use an aFlex?
  Custom App Traffic Handling
  Application Enhancements
  Traffic Steering
  Security
  Rate-limiting
  System based Logging ……etc……

## Slide 113: 5 Basic Parts of an Aflex
Events:
  Triggered based on client/server packet and/or connection flow.
Operators:
  A descriptive string representing a rational or logical operation to be executed.
Commands:
  Used on elements within the packet flow headers in order to gather data and provide aFleX functionality
Variables:
  Used to store information to memory to be recalled when needed.
Conditionals:
  Control structure in programming that allows you to create a logical flow within your code

## Slide 114: aFlex Example for ‘Event’
# rewrites relative and absolute redirects to absolute HTTPS redirects
Http request event
Http response event
when HTTP_RESPONSE {
if { [HTTP::is_redirect] } {
if { [HTTP::header Location] starts_with "/" } {
HTTP::header replace Location "https://$host[HTTP::header Location]"
} else {
HTTP::header replace Location "[string map {"http://" "https://"} [HTTP::header Location]]"
}
}
}
when HTTP_REQUEST {
set host [HTTP::host]
}

## Slide 115: Events triggered on TCP vPort
Client
Thunder
Server
SYN
SYN
SYN-ACK
CLIENT_ACCEPTED
LB_SELECTED
SERVER_CONNECTED

## Slide 116: Events triggered on TCP-Proxy vPort
Client
Thunder
Server
SYN
SYN
SYN-ACK
CLIENT_ACCEPTED
LB_SELECTED
SERVER_CONNECTED
SYN-ACK
ACK

## Slide 117: Events triggered on HTTP vPort
Client
Thunder
Server
SYN
SYN
SYN-ACK
CLIENT_ACCEPTED
LB_SELECTED
SERVER_CONNECTED
SYN-ACK
ACK
HTTP-Req
ACK
HTTP-Req
HTTP-Respose
HTTP_REQUEST
HTTP_REQUEST_SEND
HTTP_RESPONSE

## Slide 118: Events triggered on HTTPS vPort
Client
Thunder
Server
SYN
SYN
SYN-ACK
CLIENT_ACCEPTED
LB_SELECTED
SERVER_CONNECTED
SYN-ACK
ACK
ACK
HTTP-Req
HTTP-Respose
HTTP_REQUEST
HTTP_REQUEST_SEND
HTTP_RESPONSE
CLIENT-HELLO
SERVER-HELLO
CCS FINISH
HTTP-Req
CLIENTSSL_HANDSHAKE
CLIENTSSL_CLIENTCERT

## Slide 119: Events triggered on UDP/DNS vPort
Client
Thunder
Server
CLIENT_ACCEPTED
LB_SELECTED
CLIENT_DATA
DNS_REQUEST
DNS_RESPONSE
UDP/DNS Request
UDP/DNS Request
UDP/DNS Response
UDP/DNS Response

## Slide 120: aFlex Example for ‘Operator’
when HTTP_REQUEST {
if { [string tolower [HTTP::uri]] ends_with "cgi" } {
pool cgi_pool
} elseif {[string tolower [HTTP::uri]] starts_with "/abc" } {
pool abc_servers
}
}
aFleX Operators

## Slide 121: aFlex Operator Types:
Relational operators
  contains, matches, equals (eq, ==), starts_with, ends_with
    Logical operators
      not (!), and (&&), or (II)
    Regular expressions
      matches_regex, regexp, regsub, ...etc…

## Slide 122: aFlex example for ‘Command’ (2 types)
when HTTP_REQUEST {
if {[HTTP::host] equals www.a10.com} {
snatpool snat_1
pool web_sg1
}
else{
snatpool snat_2
pool other-sg
}
}
aFleX Namespace Command
aFleX Global Command

## Slide 123: 5 Basic Parts of an Aflex
Events:
  Triggered based on client/server packet and/or connection flow.
Operators:
  A descriptive string representing a rational or logical operation to be executed.
Commands:
  Used on elements within the packet flow headers in order to gather data and provide aFleX functionality
Variables:
  Used to store information to memory to be recalled when needed.
Conditionals:
  Control structure in programming that allows you to create a logical flow within your code

## Slide 124: aFlex example for ‘Variable’
  String
  set var2 “ATen”
  log “What company Rocks? $var2 !!!”
  Integer (Note: TCL will initiate a numeric variable as a string and translate it to an integer if needed by the context of usage)
    set var 9
    set ten [expr $var + 1]
    Log “What company Rocks? A$ten !!!”
aFleX Variable
aFleX Variable

## Slide 125: aFlex example for ‘Conditionals’
if { [LB::status node $server port $::PORT tcp] equals "up“ } {
log “the server $server is up”
} else {
log “the server $server is down”
}
  switch [LB::status node $server port $::PORT tcp] {
  "up" { log " the server $server is up" }
  "down" { log "the server $server is down" }
  }

## Slide 126: How is an aFlex executed?
Commands within the same event are executed in a sequential fashion.
when HTTP_REQUEST {
set host [HTTP::host]
if { [info exists ::SG_ARRAY($host)] } {
log "host $host -> pool $::SG_ARRAY($host)"
pool $::SG_ARRAY($host)
}
}

## Slide 127: Can I bind more than one aFlex under the same vPort?
When multiple aflex’s are bound to the same vPort as seen below, what specifies the order of execution –
what message below will be logged first?
  slb virtual-server aflexlog 192.168.44.107
  port 80 http
  aflex testing2
  aflex testing1
Aflex Testing 1:
when CLIENT_ACCEPTED {
set ip [IP::client_addr]
Log " aflex1 client IP = $ip"
}
Aflex Testing 2:
when CLIENT_ACCEPTED {
set ip [IP::client_addr]
Log " aflex2 client IP = $ip"
}

## Slide 128: ADC-DDOS Feature

## Slide 129: IP anomaly
• Frag – Drops all IP fragments, which can be used to attack hosts that run IP stacks with known vulnerabilities in
their fragment reassembly code
• IP-option – Drops all packets with IP options
• Land-attack – Drops spoofed SYN packets that contain the same IP address as the source and destination. These
packets can be used to launch an “IP land attack”.
• Zero-length TCP window
• Out-of-sequence packet
• Ping-of-death – Drops all jumbo ICMP packets, which are also known as “ping of death” packets
• TCP-no-flag – Drops all TCP packets that have no TCP flags set
• TCP-SYN-FIN – Drops all TCP packets in which both the SYN and FIN flags are set
• TCP-SYN-frag – Drops incomplete (fragmented) TCP Syn packets, which can be used to launch TCP Syn flood
attacks

## Slide 130: IP anomaly Configuration
vThunder(config)# ip anomaly-drop ?
bad-content bad content threshold
drop-all drop all IP anomaly packets
frag drop all fragmented packets
ip-option drop packets with IP options
land-attack drop IP packets with the same source and destination addresses
out-of-sequence out of sequence packet threshold
packet-deformity drop packets with deformity
ping-of-death drop oversize ICMP packets
sampling-enable Enable baselining
security-attack drop packets causing security attack
tcp-no-flag drop TCP packets with no flag
tcp-syn-fin drop TCP packets with both syn and fin flags set
tcp-syn-frag drop fragmented TCP packets with syn flag set
zero-window zero window size threshold

## Slide 131: Policy Based Server Load Balancing (PBSLB)
1.1.1.0/24
2.2.2.0/24
3.3.3.0/24
Select service-group SG1
Select service-group SG2
SG1
SG2
Drop the request

## Slide 132: PBSLB Configuration
Create a BW list (ADC>BW-List>Create)
1.1.1.0/24 2 ;
2.2.2.0/24 4 ;
3.3.3.0/24 6 ;
Create Policy template
  ACOS(config)# slb template policy bw1
  ACOS(config-policy)# bw-list name bw1
  ACOS(config-policy)# bw-list id 2 service-group SG1
  ACOS(config-policy)# bw-list id 4 service-group SG2
  ACOS(config-policy)# bw-list id 6 drop
  Bind the template with Virtual Service
  ACOS(config)# slb virtual-server PBSLB_VS1 10.10.10.10
  ACOS(config-slb vserver)# port 80 http
  ACOS(config-slb vserver-vport)# template policy bw1

## Slide 133: SYN-Cookie
Client
Attacker
Thunder
Thunder
Server
Server
SYN
SYN-ack(with SYN-cookie)
ACK
SYN
SYN
SYN-ack(with SYN-cookie)
SYN
SYN-ack(with SYN-cookie)
SYN
SYN-ack(with SYN-cookie)
ACOS(config)# slb virtual-server vip1
ACOS(config-slb vserver)# port 80 tcp
ACOS(config-slb vserver-vport)# syn-cookie

## Slide 134: DNS Application Firewall (DAF) Overview
Reduce load for protected servers (~70%)
  Legitimate DNS traffic allowed only
  Predictable load
  Increases capacity while freeing resources to address increased load
    DNS Pre-fetching (or Pre-Resolving) prepared
Increased security for backend servers
  Quarantine malicious traffic for inspection (or denial)
  Guarantee uptime regardless of DDoS attacks
Target: Customers running a large DNS infrastructure
  Good Target: Typically Service Providers
  Bad Target: Enterprise with outsourced DNS infrastructure
Malicious and
Invalid Non-DNS
Traffic on Port 53
“Zombies”
Infected Clients
Generating Requests
Regular Clients Perform as Expected
Optional Malicious and Invalid Traffic Redirection
Standard CPU Usage
Denied
Surge Protection
Allowed

## Slide 135: DNS Application Firewall Function
Performs sanity checks on DNS client queries
  In some cases of DNS Flood, DNS queries are sent to UDP port 53 without containing a valid DNS Request header. This type of attack is known as a DNS UDP Flood attack. The Thunder ADC can discard the invalid requests.
Also provides connection-rate limiting for "look-alike" valid DNS requests flooded by a botnet.
  This protection helps the target DNS server avoid overload

## Slide 136: Debugging

## Slide 137: AXDEBUG
AX equivalent of the open source “tcpdump”. Captures packets, ready to view in Wireshark.
Only captures packets that come to the CPU, packets sent from the ASIC/FPGA are not captured; e.g. HW SYN COOKIE.
Number of files captured == number of data CPU’s. Control CPU traffic is not captured.
Supports brief mode, detail mode and save mode.
“Brief and save” (capture brief save <FILENAME>) mode as well as “detail and save” (capture detail save <FILENAME>)mode are supported.

## Slide 138: AXDEBUG (cont.)
Filter content:
Layer 3 Protocol: IP/ARP/IPv6
Layer 4 Protocol: TCP/UDP/ICMP
Source/Destination: IP/PORT/MAC
IP Protocol based filtering is also supported.
E.g. IP Protocol 89 for OSPF

## Slide 139: AXDEBUG (cont.)

## Slide 140: AXDEBUG Commands (cont.)
Example:
  AX# axdebug
  AX(axdebug)#filter 1 // Define a filter
  AX(axdebug-filter:1)# ip 10.60.60.60 /32
  AX(axdebug-filter:1)# exit
  AX(axdebug)# count 0 // Capture unlimited # of packets
  AX(axdebug)# timeout 0 // No timeout, By default timeout is 5 min.
  AX(axdebug)# incoming // Capture incoming traffic
  AX(axdebug)# outgoing // Capture outgoing traffic
  AX(axdebug)# capture save <FILENAME> // Capture the output to a file
See the filter:
  AX(axdebug)# show axdebug filter
  axdebug filter 1
  ip 10.60.60.60 /32

## Slide 141: AXDEBUG Commands (cont.)
Status of the capture:
  AX(axdebug)#show axdebug status
  axdebug is enabled
  unlimited seconds left
  debug incoming interface all
  debug outgoing interface all
  unlimited packets left
  Captured packet length 1518
  cpu#1 captured 0 packets.
  cpu#2 captured 0 packets.
  cpu#3 captured 0 packets.
  cpu#4 captured 0 packets.
  cpu#5 captured 0 packets.
  cpu#6 captured 0 packets.

## Slide 142: AXDEBUG Commands (cont.)
Size and details of the capture:
AX(axdebug)#show axdebug file
-----------------------------------------------------------------------------------------------------------------------------------------------
Filename | Size(Byte) | Date
-----------------------------------------------------------------------------------------------------------------------------------------------
VRRP | 300144 | Tue Aug 2 10:30:10 2011
AXDEBUG | 1996534 | Fri Apr 13 13:12:25 2012
TACACS_CAPTURE | 192 | Sun May 22 22:08:45 2011
LACP | 41808 | Fri Jan 13 12:37:38 2012
OSPF_CAPTURE | 3958 | Mon Mar 19 14:45:12 2012
ISIS | 145906 | Thu Mar 29 12:04:37 2012
-----------------------------------------------------------------------------------------------------------------------------------------------

## Slide 143: AXDEBUG Commands (cont.)
Stop the axdebug capture:
  AX# no axdebug
Export the file:
  AX# export axdebug <FILENAME> use-mgmt-port scp://<IP><PATH>

## Slide 144: DEBUG Packet
Flow/Session based debugging. Both Brief and detail mode are available.
Detail mode dumps out the packet in Hex.
Has the option to filter packets based on L3 IP and L4 protocol/port, CPU #, Interface.
Can save the output of debug packet to a file.
Count 0 is used to capture unlimited packets.
Note: Don’t forget “no debug packet” after you are done with the Debugging session.

## Slide 145: TCS

## Slide 146
Course Overview
Why TCS?
Typical topology and traffic flow
Network subnets
Configs: SLB, Routing, Spoofing
Show session output
Layer 7 TCS

## Slide 147: Why is there a need for TCS?
Improve response time
  Cached response returns to client quicker
  No need to send the request to the real server every request
Reduce bandwidth demand
Ultimately, improve client experience

## Slide 148: Typical Topology and Traffic Flow
Client
Server
Server
Client
Hit the cache!
Client
Cache Server
Server

## Slide 149: Typical Topology and Traffic Flow
Client
Server
Miss the cache!
Server
Cache Server
Client
Cache Server
Cache Server
Cache Server

## Slide 150: How does it work…
From Client to Cache Server:
  SLB traffic
  Thunder operating as a Load Balancer
From Cache Server to Real Server:
  Routing traffic
  Thunder operating as a Router

## Slide 151: Typical Topology and Traffic Flow
Client
1.1.1.2
1.1.1.1
2.2.2.1
2.2.2.2
3.3.3.1
3.3.3.2

## Slide 152: SLB Config
slb server cache_server 2.2.2.2
no health-check
port 80 tcp
no health-check
!
slb service-group sg tcp
member cache_server:80
!
!
slb virtual-server wildcard 0.0.0.0 acl 100
port 80 tcp
name _wildcard_v4_100_TCP_80
service-group sg
no-dest-nat
interface ethernet 1
ip allow-promiscuous-vip
access-list 100 permit ip any 1.1.1.0 0.0.0.255

## Slide 153: Spoofing Cache
Use Client IP 1.1.1.2 instead of Cache Server IP 2.2.2.2 as source IP when forward request to the real server
Client
1.1.1.2
1.1.1.1
2.2.2.1
2.2.2.2
3.3.3.1
3.3.3.2

## Slide 154: Two additional steps to enable Spoofing
Enable cache spoofing on the AX interface connected to the cache server
interface ethernet 2
ip address 2.2.2.1 255.255.255.0
ip cache-spoofing-port
The real server configuration for the cache server, enable spoofing cache support
slb server cache_server 2.2.2.2
no health-check
spoofing-cache
port 80 tcp
no health-check

## Slide 155: Show session output
Prot Forward Source Forward Dest Reverse Source Reverse Dest Age Hash Flags Type
------------------------------------------------------------------------------------------
Tcp 15.15.15.15:49011 51.51.51.100:80 51.51.51.100:80 15.15.15.15:49011 0 2 NSe0 TCS
Tcp 15.15.15.15:49011 51.51.51.100:80 51.51.51.100:80 15.15.15.15:49011 0 2 NSe0 SLB-L4

## Slide 156: Layer 7 TCS
Send requests for particular url to cache server, other requests to edge router
The idea is to control the traffic flow based on L7 url
VIP config is the same except for vport
slb virtual-server wildcard 0.0.0.0 acl 100
port 80 http
name _wildcard_v4_100_TCP_80
service-group sg
no-dest-nat

## Slide 157: L7 TCS Config
Two service groups: one for the cache server, the other for the edge router
slb server cache_server 2.2.2.2
no health-check
spoofing-cache
port 80 tcp
no health-check
!
!
slb service-group sg tcp
member cache_server:80
slb server default_gateway 3.3.3.2
no health-check
port 80 tcp
no health-check
!
slb service-group sg2 tcp
member default_gateway:80

## Slide 158: L7 TCS Config
HTTP template with url-switching, implementing the L7 control
slb template http http_tmp
url-switching starts-with /tours service-group sg
!
!
slb virtual-server wildcard 0.0.0.0 acl 100
port 80 http
name _wildcard_v4_100_HTTP_80
service-group sg2
template http http_tmp
no-dest-nat

## Slide 159: L3V Virtualization

## Slide 160: Partitioning and Layer 3 Virtualization (L3V)
  The AX can be separated, or “partitioned”, allowing it to run different configurations at the same time, say for various companies, or for different departments within an organization.
  L3V is a feature you can enable on each individual partition, allowing each partition to have its own network resources

## Slide 161: Why L3V?
By enabling L3V on a partition, each partition is completely isolated from the others.
Resources used/created in one partition does not conflict with resources in a different partition.
Each partition that has L3V enabled can own the following resources for itself:
  Layer 2 Resources:
    Static MAC entries
  Layer 3 Resources:
    IP addresses
    ARP entries
    Routing table
  SLB Resources:
    Real servers
    Virtual-servers
    Service groups
    Templates
    Health monitors
    Cert and keys
    aFlex scripts

## Slide 162: Types of Partitions
Shared
  This is the default partition. There is only one shared partition.
Private
  You can create multiple private partitions, as needed.
Shared partition |  | 
Partition A | Partition B | Partition C

## Slide 163: Types of Partitions
Shared partition (default)
  By default, all configuration is created under this shared partition
  If no partitions are created, you are in the shared partition.
  Only admins with read-write privilege can make changes in the shared partition. All admin have the ability to view the shared partition’s configuration.

## Slide 164: Types of Partitions
Private partitions
  There are no private partitions by default.
  A read-write admin must create them, as needed.
  Private partitions can only be accessed by partition admins assigned to it, and by admins with read-write or read-only privileges.

## Slide 165: VRRP

## Slide 166: HA VRRP-A: Overview
VRRP-A is virtual mac based redundancy protocol for thunder devices
VRRP-A can provide redundancy for the following IP resources:
  Virtual server IP addresses (VIPs)
  Floating IP addresses used as default gateways by downstream devices
  IPv6 NAT pools
  IPv4 NAT pools
  IPv4 static range lists and individual mappings for inside source NAT
Partition Support – only with L3V enabled

## Slide 167: Hello Messages
VRRP-A Hello Messages
  By default, the active device sends hello messages every 200 milliseconds (ms). Standby devices, by default, wait a maximum of 1 second for a hello message. If no hello message is received within 1 second, failover occurs.
  Hello Message Destination Addresses
  VRRP-A sends hello messages to the following addresses:
  IPv4 multicast address 224.0.0.210, MAC address 01:00:5e:00:00:D2
  IPv6 link-local multicast address FF02::D2, MAC address 33:33:00:00:00:D2
Dynamic Priority Reduction

## Slide 168: Failover Triggers
  Failover Triggers
    Standby stop receiving hello message
    VRRP-A priority on active device is manually reduced below the standby priority, and pre-emption is enabled
    VRRP-A priority on active device is dynamically reduced below the standby priority
    Force-self-standby

## Slide 169: High Availability – VRRP-A
Standby->Active new Active Thunder sends gratuitous ARPS for IP addresses under VRID Control
VIPs that are assigned to an VRID
Floating IP address, if configured
NAT pools assigned to an VRID
Devices that receive the ARPs learn MAC address and update their forwarding tables
Basically, Thunder sends ARPs immediately
Then, Thunder sends gratuitous ARPs every 30 seconds

## Slide 170: Active Device selection
Device Boot
Weights equal ?
Device with highest weight is selected as Active
Preemption disable?
No
Yes
Yes
Device are all active and the first device that receives the heartbeat packet from other active device becomes the standby
No
Device with highest priority is selected as Active

## Slide 171: VRRP-A Configuration
Enable VRRP-A
  vrrp-a common
  device-id 1
  set-id 1
  enable
Enable VRRP-A on interface
  vrrp-a interface ethernet 1
  vrrp-a interface ethernet 2
Configure VRID
  vrrp-a vrid 0
  floating-ip 1.1.1.3
  blade-parameters
  priority 250
  tracking-options
  interface ethernet 1 priority-cost 100
  interface ethernet 2 priority-cost 100
  vrrp-a common
  device-id 2
  set-id 1
  enable
  vrrp-a interface ethernet 1
  vrrp-a interface ethernet 2
  vrrp-a vrid 0
  floating-ip 1.1.1.3
  blade-parameters
  priority 200
  tracking-options
  interface ethernet 1 priority-cost 100
  interface ethernet 2 priority-cost 100

## Slide 172: Tracking Options
vThunder-Active(config-vrid:0-blade-parameters-track...)#?
    bgp Bgp tracking
    gateway VRRP-A tracking gateway
    interface Interface tracking
    route Route tracking
    trunk trunk tracking
    vlan VLAN tracking

## Slide 173: Thank-You

## Slide 174: A10 icon library
Updated February 2018

## Slide 175
Thunder Hardware
Thunder HVA
Thunder SPE
Bare Metal
vThunder - virtual
vThunder - cloud
ADC
TPS
CGN
SSLi
CFW
HVA
aGalaxy
Lightning
aCloud
Harmony
Controller
Server
Virtual Server

## Slide 176
Thunder Hardware
Thunder HVA
Thunder SPE
Bare Metal
vThunder - virtual
vThunder - cloud
ADC
TPS
CGN
SSLi
CFW
HVA
aGalaxy
Lightning
aCloud
Harmony
Controller
Server
Virtual Server

## Slide 177
Automobile
Corporate / Enterprise
Digital Advertising
Education
Education / Online Education
Finance / Banking
Government
Health Care
Insurance
Hosting
Manufacturing
Online Gaming
Retail
School
Mobile
Service Provider
Service
Provider
Web Giants

## Slide 178
AAM
ALG Support
Analytic
DevOps Ready
Gateway
GSLB
High-Density Partition
SLB
ICAP
Intelligent Threat Protection
IPv4<->IPv6
IPsec VPN
Multi-Tenancy
Traffic Mirroring
Open API Integration
Single Sign-On

## Slide 179
Data Base
Firewall
Mobile
Desktop
Router
Laptop
Switch
Tablet
Signal Tower
CPU
Home Router
Deploy

## Slide 180
Data Base
Firewall
WAF / Web Application Firewall
Mobile
Key Storage
Firewall - Breached
Data Center Firewall
Secured Laptop
Cloud Storage
DNS Firewall
Desktop
Webinar
Router
High-Performance Firewall
Laptop
Entertainment Devices
Switch
Firewall LB
Tablet
Interactive Service Map

## Slide 181
Lock On / Secured
Lock Off / Non Secured
Security / Openness
High-Performance Security
Secured ADC
Extend Life Security
High-Performance SSL Security
SSL Encrypted
SSL Decrypted
Cloud
Internet
IPv4 Cloud
IPv6 Cloud
Cloud Scalability
Secured Cloud
Non Secure Cloud
Cloud Automation / Agility
Cloud Ready
Cloud Controller
Hybrid Cloud
Threat Intelligent Cloud
Real-Time Analytic Via SaaS
Container Cloud
Private Cloud
Public Cloud
Cloud Deployment
COTS
Traditional Deployment

## Slide 182
APP
Application Management
Application Server
Application Server
Application Analytic
Infected Application
eMail
Window
Management Orchestration
Cloud Orchestration
SDN Controller
Scripting
Advanced Logging
Browser Window
Admin Portal
Feature Licensing
Software
Easy to Manage
SQL Injection
Third-Party Integration
White Paper
Folder
Open Folder
Infected Folder

## Slide 183
Document / Data
Infected Doc
Patent
All Inclusive Licensing
Certificate
Policy Enforcement / Service Reporting
Policy Management
Download
Central Policy Management
Medical Data
Flexible License
Encrypted Data
Attachment
Infected Attachment
Programmatic Policy Engine
Incident Response
High-Speed Logging
Log / Clipboard

## Slide 184
User
Secured User
Non Secured User
Customized
Support
24-7 Support
Professional
Good/Clean User
Access Denied
Cloud User
Customer
Happy Customer
Police
Student
Engineer / IT
Infected User
Infected User
Group Experts
Group of Users
Parental Control
Group of Users

## Slide 185
Hacker
Hacker
Prankster
Hacktivists
Bug
DDoS Attack
Anti-Virus
Trojan
ID Breached
Botnet
Hacker
Threats
Infected APP
Infected Laptop
Botnet Attack
Infected App

## Slide 186
Check
X
Denied
Denied
Question
Synchronizing
Refresh
Performance High
Performance Low
Target
Targeted Bug
Problem
Detection / Inspection
Extend Life
Full Visibility
Visibility
No Visibility
Key
Search
Solution
ID
Gear
Gear - Round
Gears
Gears
Data Filtering
Data Filtering
Always On

## Slide 187
Profit-Lose
Profit-Gain
Loading-Slow
Responsive
Superior
Customizing
Tool
Media-Image
Media-Film
Media-Play
Media-Web
Media-Music
Media-Headset
Media-Video
Chat
Group Chat
Positive Reputation
Partnership
Easy Access
Connectivity
Contact
Consolidate
Billboard
retargeting
Share Intelligence
Large Earning
Saving
Price Down / Cost Down

## Slide 188
Money
Location
News
Priority Pyramid
Priority 1
Priority 2
Priority 3
Priority 4
Massive Performance and Scale
Increase Appliance Capacity
Increase Appliance Capacity
Scalability
High-Performance Software
Feature
Dynamic Traffic Management
Symmetric
Proactive
Reactive
TAP (Out Of Band)
Intelligence Service
Performance with Precision
Multi-Vector DDoS Protection
Powerful & Efficient
DDoS Protection
Enable BI-Model IT
Full Spectrum Protection
Threat Intelligence Protection
Customize and Integrate

## Slide 189
Integrated Protection
Mitigation
Flexible High- Performance Visibility
Traffic Mirroring Support
SSL
URL Category
Decrypt SSL Once Inspect Multiple Times
SSL Decryption
Explicit Proxy Support
Multiple Ciphers
Secure HSM
Data Acceleration and SSL Offload
ALGs
Advanced CGNAT
Extend Life of IPv4
CGNAT
Flexible Deployment (Cross Platform)
Protection & Performance
Stateful L4 FW
Connection Rate Limit
URL Filtering
Security Device Scaling
Centralized Cloud Management
Hybrid Service
Enhance CI/CD
Elastic and Secure
Elastically Scale
Optimize and Accelerate Traffic

## Slide 190
Access Control
Agility
Application
Acceleration
Application
Availability
aXAPI REST-based Programmability
Compression
Connection Rate Protection
Data Acceleration
Defeat Cyber Attacks
Elastic WAF
Eliminate 3rd-Party Costs
High Capacity
HTTP/2
In-Memory Caching
Layer 4-7
Multi-Dimensional Security
Optimize and Accelerate
SDN / NFV Ready