## Slide 1
LB Redundancy for Geo-Graphic Sites

## Slide 2: Option #2 Configuring VRRP Across Sites over Private IP
Site B
Site A
Appdirector
Appdirector
L2 Domain to Carry
VRRP hello
Private Cloud
VIP1
VIP 2
VIP 3
Configured as
VRRP Owner for VIP1 and VIP 2

## Slide 3: Option #1 Configuring VRRP Across Sites over Public IP
Site B
Site A
Appdirector
Appdirector
L2 Domain to Carry
VRRP hello
Public Cloud
VIP1
VIP 2
VIP 3
Configured as
VRRP Owner for VIP1 and VIP 2

## Slide 4: Challenges with Option#1 and Option#2
In both the options (1 and 2), need of extending L2 vlan between sites is must since VRRP hello should be seen to each LB and these are multicast packets
Apart from that if this L2 channel breaks then there could be a condition where both the LB will announce themselves as master causing loop in network
With Public IP approach, need to ensure same subnet Public IP is allocated on both sites which could be difficult if ISP’s at each location are different.

## Slide 5: Option#3 Global IP using Anycast with BGP
172.19.239.x/24
172.19.240.x
Site B
Site A
BGP
172.31.2.x
Appdirector
Appdirector
VIP
172.31.2.132
AD IP :
172.31.2.138
VIP : 172.31.2.132
AD IP : 172.19.239.138
Route
Injection in to BGP
Domain with Metric 5
Route Injection in to BGP
Domain with Metric 50
Route
Injection in to BGP
Domain with Metric 100
Internet

## Slide 6: Option#3 Global IP using Anycast with OSPF
10.87.248.32/28
LB Subnet- 10.87.248.96/29
Site B
Site A
OSPF
LB Subnet- 10.87.248.48/29
Appdirector
Appdirector
VIP
10.87.248.36
AD IP :
10.87.251.91
VIP : 10.87.248.36
AD IP : 10.87.251.23
Route
Injection in to OSPF
Domain with Metric 5
Route Injection in to OSPF
Domain with Metric 50
Route
Injection in to OSPF
Domain with Metric 100
Internet
Secondary LB interface IP : 10.87.248.102
Primary LB interface IP : 10.87.248.54
Area 0.0.0.6
Router ID: 10.87.248.54
Router ID: 10.87.248.102
SR1: 10.87.248.50
SR2: 10.87.248.51
SR1: 10.87.248.98
SR2:10.87.248.99

## Slide 7: Overview
Radware Load Balancer will participate in the service provider routing protocol
Routes with different metric will be announced into service provider routing domain
Routes will be announced for Virtual IP which is common on both DC and DR
Radware Load balancer’s interface will become next hop for virtual IP
3 IP subnets (need not be /24) are required for proposed architecture
  For Radware load balancer at DC
  For Radware load balancer at DR
  For Virtual IP common in DC and DR
Service provider should accept and announce /32 IP routes in their routing domain
Allowed protocol for above architecture are
  OSPF
  BGP
Service Provider gateway router should enable peering with Radware Load Balancer for routing protocol

## Slide 8: Challenges
Due to large dependency on routing, this approach needs support to be extended by Service provider as well since service provider needs to accept the routes from customer
Implementation of BGP with service provider could be complex at time and thus rendering troubleshooting difficult at times.

## Slide 9: Option#4 GSLB with DNS
Page 9
www.site.com
www.site.com
VIP-A
VIP-B
Client’s Local DNS Server
www.site.com ?
site.com DNS Server
www ?
Zone File
www IN NS AD-A
www IN NS AD-B
www ?
www.site.com = VIP-B
www.site.com = VIP-B
Go ask:
NS AD-A, NS AD-B
AppDirector B
AppDirector A

## Slide 10: Overview
Appdirector on each site will become Authoritative Name Servers for the domain hosted
Each AD on Site will have its own VIP for site www.site.com
When DNS query comes to DNS registrar, it points to NS1 and NS2.
These NS1 and NS2 are nothing but AD located in each geographical site
On receipt of the DNS query, AD on that site, depending on mode of config will share the VIP of the site.
The mode supported could be active – active or active backup
The failover can be triggered when All real servers are down or complete site is down
LB on both site communicate with each other for exchange of information and keep-alive.
Admin is in total control of how to server the traffic to end user.

## Slide 11
Thank You